## Slide 1
InfraPulse
Photo-based defect detection and priority maintenance routing
A resident photographs a defect. The system identifies it, decides how urgent it is, and sends it to the right team — with nobody sorting the pile.
Team Shauryas · Takneek'26
Notes: InfraPulse turns a photograph of a building defect into a triaged, routed maintenance job. No manual categorisation anywhere in the flow.

## Slide 2
THE PROBLEM
Every complaint is treated as equally urgent
1
Unreported until dangerous
Spalling and cracked tiles go unnoticed until they become a safety hazard or a costly repair.
2
Manual inspection is slow
Facility teams rely on walking the building and on complaints typed in free text.
3
No sense of risk
A loose paint flake and exposed structural rebar enter the same undifferentiated list.
What triage should look like
Exposed rebar
50.8
Crack network
46.9
Cracked floor tile
39.3
Loose paint flake
15.0
Ordered by what the photograph shows
Notes: The core failure is not that complaints go missing. It is that they all look the same once filed.

## Slide 3
HOW IT WORKS
One photograph, five automatic steps
1
Classify
Our fine-tuned CNN names the visible defect
2
Route
Defect maps to Structural, Functional or Performance
3
Measure
Grad-CAM gives extent; pixel statistics give severity
4
Score
The documented priority formula produces a number
5
Queue
Placed in that category's live queue, in order
No step asks the resident or the staff member to choose a category or a priority. Both are produced by the system from the image alone.
Notes: Walk left to right. Emphasise that the resident only uploads a photo, address and description.

## Slide 4
DETECTION
Trained by us, on data we assembled
Four classes, three categories
Spalling to Structural. Stagnant water to Functional. Cracked tiles and paint peeling to Performance.
5,418 images from five public sources
Assembled with an explicit label-by-label map after keyword matching silently pulled 1,125 'tile loss' boxes into cracked tiles.
ResNet18, ImageNet-pretrained
All layers fine-tuned; backbone at a low learning rate so the pretrained features are nudged rather than overwritten.
Problem-statement compliance
Inference runs inside our own application, on CPU, using weights we trained.
No external AI or ML inference service is contacted at any point.
The only pretrained starting point is ImageNet — a general-purpose dataset, explicitly permitted.
No defect, crack or building-damage checkpoint anywhere in the pipeline.
Notes: If asked about rules: ImageNet backbones are named in the PS as permitted. What is banned is a checkpoint pretrained on defect data, which we never used.

## Slide 5
EVALUATION
98.05% on a held-out test set
98.05%
Test accuracy
97.86%
Macro F1
819
Held-out images
Chart: 
| Stagnant water | Paint peeling | Cracked tiles | Spalling
F1 score | 0.9959 | 0.982 | 0.9806 | 0.956
Reading the errors
Spalling is the weakest class, and its dominant error is five images read as paint peeling.
That is the physically sensible confusion — both are a surface layer coming away from a wall, and separating them depends on depth, which a single photograph barely carries.
A model exploiting dataset artefacts would fail in scattered, meaningless ways. Ours concentrates its mistakes on the one pair a human also finds ambiguous.
Notes: Stagnant water is 245 of 245. Water is glossy and reflective and shares no visual vocabulary with dry masonry.

## Slide 6
PRIORITY — 40% OF THE RUBRIC
Urgency measured from the photograph
priority_score = 100 × base_weight × ( 0.5 × severity + 0.5 × extent )
extent
Grad-CAM on our own network highlights the pixels that drove the decision. The highlighted fraction of the image is the extent — no second model, no extra labels.
severity
Inside that region only: local contrast, edge density, and how far it deviates from the surrounding surface.
base_weight
Cracked tiles 1.00, paint peeling 0.75 — the ordering the problem statement fixes for the Performance category.
Same category, measured apart
Exposed rebar
severity 0.796 extent 0.220
50.83
Loose paint flake
severity 0.109 extent 0.291
14.99
A 3.4× gap, produced by measurement — not by a rule naming those defects.
Notes: Deterministic: the same photograph always yields the same score. Every input is computed live from the upload. Ties break by submission time, oldest first.

## Slide 7
METHOD
We tried to break our own number
Our first run reported 98.03%. We did not trust it.
The risk
Many images are crops of one photograph. A random split puts one crop in training and another in testing — the model has already seen the answer, and the score is fiction.
What we found
Roboflow ships augmented twins of each photo under different filenames. Measured duplication: 2.8× in one source, 3.0× in another.
The fix
Split by source photograph, grouping on the filename stem before '.rf.', capped at three crops per photo, with an assertion that no photo spans two splits.
After the fix the score held at 98.05%. The number survived a deliberate attempt to break it — which is the only reason we quote it.
Notes: This slide is the differentiator. Most teams report whatever their first split gives them.

## Slide 8
THE APPLICATION
Two portals, three live queues
R
Resident
Register and log in
Submit name, address, description, photo
See the detected defect and category
Track status and queue position
Resolved complaints stay in history
S
Staff
Log in to one category only
See that queue, ranked by priority
Advance Submitted to Assigned to In Progress to Resolved
Resolved leaves the live queue immediately
New complaints appear without a refresh
FastAPI · SQLite · server-rendered pages · one deployable process, one URL
Notes: Queues poll every five seconds, so a new complaint appears in the staff queue without anyone refreshing.

## Slide 9
LIMITATIONS AND NEXT STEPS
What it cannot do yet
Limitations
Source concentration
Each class draws mostly from one or two datasets, so part of the accuracy may reflect recognising the dataset rather than the defect.
Tile domain mismatch
Our cracked-tile images are mostly mosaic facade tiles. On damaged hostel skirting the model returned paint peeling at 46% confidence.
Closed-set classification
Only four labels exist, so a damp stain is forced into the nearest one.
Where we would go next
Photograph the real buildings
A few hundred images from the hostels and blocks this will serve addresses both gaps above directly.
Show a confidence threshold
Below 60%, offer the top two candidates and flag for staff confirmation instead of asserting one answer.
Add an out-of-scope class
Train a fifth class on stains, algae and normal walls so non-target defects are not forced into the four.
Notes: Stating the 46% miss openly is deliberate. It shows we tested outside our own distribution.

## Slide 10
Photograph in. Triaged job out.
Detection, classification, routing, priority and queueing — all from a single uploaded image, all running inside our own application.
Team Shauryas · Takneek'26
Notes: Close by opening the live URL and submitting a photograph in front of them.